## Slide 1: EKG MONITORING OVERVIEW
Dr. Jennifer Lucy
CCMA Prep 2017

## Slide 2: Anatomy of12 lead EKG

## Slide 3: 12 Lead EKG placement

## Slide 4: Chest Leads
6 chest leads are labelled as V leads and are numbered from V1-V6
Positioned in specific positions on the rib cage.
Find the 2nd Intercostal space below the collar bone. From this position, run your fingers downward across the next rib, and the next one.
The space you are in is the 4th intercostal space. Where this space meets the sternum is the position for V1.
V1 should be positioned at the 4th Intercostal space to the right of the sternum.
V2 is to be placed at the 4th Intercostal space to the left of the sternum and
V3 midway between V2 and V4.
V4 must be then positioned at the 5th Intercostal space at the midclavicular line
V5 at the anterior axillary line at the same level as V4.
V6 is to be placed at the maxillary line at the same level as V4 and V5.

## Slide 5: Peripheral Limb Leads
Peripheral leads:
RL (right leg) lead must be positioned anywhere above the ankle and below the torso.
RA (right arm) lead is to be placed anywhere between the shoulder and the elbow,
LL (left leg) lead should be positioned anywhere above the ankle and below the torso, and
LA (left arm) lead anywhere between the shoulder and the elbow.
It is very important that the ECG leads are placed correctly since incorrect placement can lead to a false diagnosis of infarction or negative changes on the ECG.

## Slide 6: 5 Lead Telemetry Lead Placement
This is the most common type of continuous monitoring
Used in Telemetry to monitor cardiac rhythm while patients are in hospital

## Slide 7: Pneumonic to remember placement
White Clouds go right over the Green fields
Black Smoke over red fire
Brown chocolate lies close to the heart

## Slide 8: 5 Lead placement

## Slide 9: Holter Monitors
Holter monitor is a small non-invasive ambulatory, portable ECG machine used to record the heart’s electrical activity in a 24–72 hour period
It correlates any symptoms (chest pain, palpitations) the patient experiences with the heart’s electrical activity at that time
Record arrhythmias that occur, providing diagnostic information about the type of arrhythmia, how long it lasts, and what might trigger it
Determine how well anti-arrhythmia medications are working

## Slide 10: Important to know
The box records and stores continuous heart rhythm data transmitted by the electrodes. The Record Box will indicate it is working by displaying the time and a “recording” message on the screen
Once the Holter Monitor is attached to the patient it must stay on the patient for the prescribed time, 24-72hrs.
Patient is allowed to go about normal activities of daily living, however they must avoid getting the Holter Monitor wet, therefore no showers or baths
Patient should record activities such as having a bowel movement or eating as this can affect reading

## Slide 11: Holter Monitor

## Slide 12: 3 Lead Monitor
In these leads, one limb carries a positive electrode and the other limb, a negative one. The three limb electrodes, I, II and III form a triangle (Einthoven's Equilateral Triangle), at the right arm (RA), left arm (LA) and left leg (LL).

## Slide 13: Counting Heart Rates Regular Rythyms

## Slide 18: Counting Irregular Rates

## Slide 20: Rhythm Check
ASYSTOLE

## Slide 21
ATRIAL FLUTTER

## Slide 22
Second degree block

## Slide 23
ATRIAL FIBRILLATION

## Slide 24
VENTRICULAR FIBRILLATION

## Slide 25
SINUS RHYTHYM

## Slide 26
VENTRICULAR TACHYCARDIA

## Slide 27
IDIOVENTRICULAR RHYTHYM

## Slide 28
SINUS TACHYCARDIA

## Slide 29: DETERMINING IF NORMAL OR ABNORMAL
Is it rhythm regular?
Is there a p wave for every qrs complex? Is the p wave upright?
Is there a QRS for every complex?
What is the PR interval ? Should be .12-.20 ( 3 to 5 large boxes)
What is the QRS Duration? Should be less that 0.12 ( 3 boxes)
What is the rate?
Below 60 Bradycardia
Above 100 Tachycardia

## Slide 30: What does the Complex mean?
P wave?
Atrial depolarization
QRS COMPLEX Ventricular Depolarization
ST segment
Initial repolarization
T wave
Ventricular Repolarization